## Slide 1: Workshop Arduino

## Slide 2: Arduino Workshop
• Background on microcontrollers
Writing a program
Connecting hardware
Actions:
Making a LED blink
Read a button
Read a sensor
Send text to computer
State machine

## Slide 3: “Microcontrollers are not scary”

## Slide 4: Products with microcontrollers
Workshop Arduino

## Slide 5: Why microcontrollers for ID?
They enable you to turn your concepts into working interactive prototypes
Can be used/developed everywhere in your career at low cost
Arduino is supported by a huge community; you can build upon existing code and hardware designs (your own or by others)

## Slide 6
Arduino Uno
Arduino MEGA
Arduino Nano
Arduino Pro Mini
Arduino Lilypad
Arduino DUE (ARM based)

## Slide 7
Atmel AVR
Microcontroller
Digital input and output pins
Power out
Reset button
Analog input pins
USB connector
Power in
Clock
“ heartbeat”
Power indicator

## Slide 8
Intelligent Control
Input
Output
The development system

## Slide 9: The development system
Microcontroller
Input
Output

## Slide 10: The development system
Input
Output
Microcontroller
Arduino board
Stabilized
power supply
Clock

## Slide 11: The development system
Input
Output
Microcontroller
Arduino board
Stabilized
power supply
Clock

## Slide 12: The development system
Input
Output
Microcontroller
Arduino board
Stabilized
power supply
Clock
Computer
USB port

## Slide 13: The development system
Input
Output
Microcontroller
Arduino board
Stabilized
power supply
Clock
Computer
USB port

## Slide 14: A microcontroller . .
Is a processor with
Low power
Low cost
Dedicated for a single task
On-board program memory
On-board data memory
I/O pins (digital and/or analog)
(Timer/counter circuits)
(Bus protocols: RS232, USB, I2C, SPI, …))

## Slide 15: Electronics: Digital Inputs
Digital input:
0 Volt: Low
5 Volt: High
2.5 Volt or floating?:
  Undefined !!

## Slide 16
Electronics : Digital sensors

## Slide 17: Electronics: Digital Inputs
External pull up Internal pull up Internal pull up (new)
pinMode(12, INPUT); pinMode(12, INPUT); pinMode(12,INPUT_PULLUP);
digitalWrite(12, LOW); digitalWrite(12, HIGH); int a = digitalRead(12);
int a = digitalRead(12); int a = digitalRead(12);
5V
Arduino
GND
100K
switch
Arduino
GND
20K
switch
5V

## Slide 18: Electronics: Analog Inputs
Analog input:
0..5 Volt to 0..1024

## Slide 19
Electronics : Analog sensors

## Slide 20: Electronics: Analog Inputs
pinMode(A0, INPUT);
Int a = analogRead(A0);
5V
Arduino
GND
10K
A0

## Slide 21: Electronics: Digital Outputs
Digital output:
0 Volt: Low
5 Volt: High
2.5 Volt? NO
PWM and average voltage for a number of duty cycles
(“PWM” : ~ pins)

## Slide 22
Electronics : Actuators

## Slide 23: Electronics: Digital Outputs
pinMode(13, OUTPUT); pinMode(11, OUTPUT);
digitalWrite(13, LOW); analogWrite(11, 186);
digitalWrite(13, HIGH);
Arduino
GND
330Ω
LED

## Slide 24: Electronics: Digital Outputs
Bang
Digital output:
0 Volt: Low
5 Volt: High

## Slide 25: Electronics: Digital Outputs
Digital output:
0 Volt: Low
5 Volt: High
External Power
< 20mA
Amp

## Slide 26: Some Hardware Limitations (Arduino Uno)
The Uno can be powered via USB or external power supply; power source is selected automatically. Usually a PC USB port is power limited to 100 mA max.
External (non-USB) power can come from an AC-to-DC adapter or battery. The adapter can be connected into the board's power jack. Leads from a battery can be inserted in the Gnd and Vin pin headers of the POWER connector.
Operating Voltage 5 V
Input Voltage (recommended) 7-12 V, (limits) 6-20 V. If the Uno is supplied with less than 7 V, the 5 V pin may supply less than five volts and the board may be unstable. If using more than 12 V, the voltage regulator may overheat and damage the board
DC Current per I/O pin max. 40 mA
DC Current for 3.3 V pin max. 50 mA
Depending on supply voltage and current usage (including the current for the processor) the voltage regulator may overheat and stop working until it has cooled down. Generally driving one servo or a few normal LEDs is the maximum.

## Slide 27: The development system
Input
Output
Microcontroller
Arduino board
Stabilized
power supply
Clock
Computer
USB port

## Slide 28: The IDE program
Arduino board
USB port
A compiled “hex”-file is
sent to the program
memory of the Arduino board

## Slide 29: The program
First, tell Arduino what it is:
Declare pins as input or output
Set global variables
This is done only once
immediately after reset
Then tell it what to do:
Read inputs
Do calculations
Set outputs
This is done continuously,
in a loop after setup is finished

## Slide 30: The program
/* Configuration:
First, tell Arduino what it is */
void setup() {
// initialize the digital pin as an output.
// Pin 13 has a LED connected on most Arduino boards: pinMode(13, OUTPUT);
}
/* Then loop:
Tell Arduino what to do */
void loop() {
digitalWrite(13, HIGH); // switch LED on
delay(1000); // wait for a second
digitalWrite(13, LOW); // switch LED off
delay(1000); // wait for a second
}

## Slide 31: Compiling and uploading code
Type code in text window
Push ‘upload’ button
Check if TX and RX Leds are blinking rapidly
If the ‘Done uploading’ message displays, the Arduino is ready.
1
2
3
4

## Slide 32: www.arduino.cc
Everything you need is www.arduino.cc
Getting started
Reference
Tutorials
Hardware examples
Software examples

## Slide 33: The Arduino Programming Environment
Compile and Upload
Verify (Compile)
Open Sketch (old: *.pde, new: *.ino)
Save Sketch
New Sketch

## Slide 34: Settings
Let the Arduino programming environment know which board you have
  “Tools” menu  “Board”
Let the Arduino programming environment know to which port the board is connected
  “Tools” menu  “Serial port”

## Slide 35: Blink
/* comment */
void setup() {
// initialize the digital pin as an output.
// Pin 13 has a LED connected on most Arduino boards: pinMode(13, OUTPUT);
}
void loop() {
digitalWrite(13, HIGH); // switch LED on
delay(1000); // wait 1000 ms
digitalWrite(13, LOW); // switch LED off
delay(1000); // wait 1000 ms
}

## Slide 36: Blink with button
The period of “Blink” is 2 x 1000 ms = 2 s
Now we want: if we push a button, the period should become 0.5 s
To do:
  Connect a button
  Read a button
  Change the “1000” in “delay” depending on the button state

## Slide 37: Blink and read button
/* comment */
void setup() {
// initialize digital pin 13 as an output.
// Pin 13 has a LED connected on most Arduino boards: pinMode(13, OUTPUT);
pinMode(12, INPUT); // initialize digital pin 12 as input.
digitalWrite(12, HIGH); // activate pull-up resistor
}
void loop() {
digitalWrite(13, HIGH); // switch LED on
delay(1000); // wait one second
digitalWrite(13, LOW); // switch LED off
delay(1000); // wait one second
}

## Slide 38: Possible hardware for Blink with button
Switch
LED

## Slide 39
void setup() {
// initialize the digital pin 13 as an output.
// Pin 13 has a LED connected on most Arduino boards: pinMode(13, OUTPUT);
pinMode(12, INPUT); // initialize digital pin 12 as input.
digitalWrite(12, HIGH); // activate pull-up resistor
}
void loop() {
if (digitalRead(12) == HIGH) {
// Do something
}
else {
// Do something else
}
digitalWrite(13, HIGH); // switch LED on
delay(1000); // wait one second
digitalWrite(13, LOW); // switch LED off
delay(1000); // wait one second
}

## Slide 40
int wait = 1000;
void setup() {
…
}
void loop() {
if (digitalRead(12) == HIGH) {
// Do something
}
else {
// Do something else
}
digitalWrite(13, HIGH); // switch LED on
delay(wait); // wait for wait msec
digitalWrite(13, LOW); // switch LED off
delay(wait); // wait for wait msec
}

## Slide 41
int wait = 1000;
void setup() {
…
}
void loop() {
if (digitalRead(12) == HIGH) {
wait = 1000; // Wait 1 sec
}
else {
wait = 250; // Wait 0.25 sec
}
digitalWrite(13, HIGH); // switch LED on
delay(wait); // wait for wait msec
digitalWrite(13, LOW); // switch LED off
delay(wait); // wait for wait msec
}

## Slide 42: Create some interaction: The “Physical Pixel” example
const int ledPin = 13; // the pin that the LED is attached to
int incomingByte; // a variable to read incoming serial data into
void setup() {
Serial.begin(9600); // initialize serial communication
Serial.println(”Good morning”); // Send text to computer
pinMode(ledPin, OUTPUT); // initialize LED pin as output
}
void loop() {
if (Serial.available() > 0) {
incomingByte = Serial.read();
if (incomingByte == 'H') digitalWrite(ledPin, HIGH);
if (incomingByte == 'L') digitalWrite(ledPin, LOW);
}
}

## Slide 43: How to proceed?
Find new functions in the reference (http://arduino.cc/en/Reference/HomePage)
Arduino playground Manuals and Curriculum (also downloads) (http://playground.arduino.cc/Main/ManualsAndCurriculum)
Don’t be scared by “Making things talk”: the book is about connecting to the internet and less to interfacing with electronics

## Slide 44: Available examples
For descriptions see http://arduino.cc/en/Tutorial/HomePage

## Slide 45: The mini project
Next week (Tuesday December 17) team presents mini project proposal (HG 3.02 Gr1 / HG 3.21 Gr2)
Sessions December 19 and January 7 no “class”, but support in and around e-Atelier/ID-Café for mini project development
January 9 (HG 4.57) team presents your mini project result (demo + mini poster)

## Slide 46: The mini project
You are free to choose your project, but:
  Use Arduino
  Use at least one input and one output
  Report on design choices (transistor, configuration, etc.)
  Draw schematics
  Present it as a prototype (user experience, packaging) !

## Slide 48: Suggestions
Make the central heating system with Arduino
μC
Temp.
Set
Heater

## Slide 49: Suggestions
Dim a LED
Make application / context
μC
Set

## Slide 50: Suggestions
Egg timer
μC
Soft
Middle
Hard

## Slide 51: Spaghetti in code, schematics and circuits
Code:
Use comments /* like this */ or // this
Use functional variable names
Use functions
Schematics:
Draw the complete circuit (correctly!!)
(component names, values)
Circuit (soldered or breadboard)
Should be structured
Use color coding in wires
Think about component placement
Otherwise:
Debugging becomes difficult
You lack evidence in your report

## Slide 52: Code
Code:
Clear variable names
Proper use of local and global variables
Functions setup() and loop() are self-explaining
Proper function names
Comments (Header)
Examples
  Bad example
  Good example

## Slide 53: Schematics

## Slide 54: Circuits

## Slide 55
Poster
Explanation
Schematic
Code
Pictures

## Slide 56
Resources
Look at wiki page:
  http://wiki.id.tue.nl/ce/AssignmentDescription
  (and checkout the “Resources” section)

## Slide 57
Finite State Machines
state OFF
LED on
Process LED step
(Notation: Finite State Machine)
button pushed
initial
state ON
LED off

## Slide 58
/*
Author : Loe Feijs
Date : 20130302
Modified : P.Peters
Date : 20131205
This example shows how to control a LED using a finite state machine. The LED goes on when the button switch is pushed. The LED goes off after 10 seconds.
*/
//connect LED, Button:
#define ledPin 9
#define buttonPin 8
Light-Time-Switch: full code

## Slide 59
Light-Time-Switch: full code
//FSM states:
#define OFF 0
#define ON 1
void setup() {
pinMode(ledPin, OUTPUT);
pinMode(buttonPin, INPUT_PULLUP);
}
void loop() {
LEDstep();
delay(10); // one step every 10 ms
}

## Slide 60
Light-Time-Switch: full code
int state = OFF; // initial state
int timer = 0;
void LEDstep(){
switch (state){
case OFF:
if (digitalRead(buttonPin)){
// change state
state = ON;
// state transition actions
timer = 1000; //10 seconds
analogWrite(ledPin,255);//max brightness
}
break;

## Slide 61
Light-Time-Switch: full code
case ON:
if (timer <= 0){
// change state
state = OFF;
// state transition actions
analogWrite(ledPin,0);
} else timer--;
break;
}
}

## Slide 63: Installation 1: The Environment

## Slide 64: Installation 2: The COM port
A “Virtual COM port” is needed to communicate with the board.
For the Arduino UNO: plug in the Arduino
On Mac OS-X, the VCP driver is installed automatically
On Windows, you have to point to the .inf file in the “drivers” directory of the Arduino software
For the Arduino Duemilanove, you have to point to the FTDI install directory which is in the “drivers” directory as well
http://arduino.cc/en/Guide/Windows
http://arduino.cc/en/Guide/MacOSX