## Slide 1: Workshop Arduino

## Slide 2: Arduino Workshop
• Background on microcontrollers
Writing a program
Connecting hardware
Actions:
Making a LED blink
Read a button
Read a sensor
Send text to computer

## Slide 3: “Microcontrollers are not scary”

## Slide 4: Products with microcontrollers
Workshop Arduino

## Slide 5: Why microcontrollers for ID?
They enable you to turn your concepts into working interactive prototypes
Can be used for many purposes in your career at low cost
Arduino is supported by a huge community; you can build upon existing code and hardware designs (your own or by others)

## Slide 6
Arduino Uno
Arduino MEGA
Arduino Nano
Arduino Pro Mini
Arduino Lilypad
Arduino DUE (ARM based)

## Slide 7
Atmel AVR
Microcontroller
Digital input and output pins
Power out
Reset button
Analog input pins
USB connector
Power in
Clock
“ heartbeat”
Power indicator

## Slide 8: The development system
Input
Output
Microcontroller
Arduino board
Stabilized
power supply
Clock
Computer
USB port

## Slide 9: A microcontroller . .
Is a processor with
Low power
Low cost
Dedicated for a single task
On-board program memory
On-board data memory
I/O pins (digital and/or analog)
(Timer/counter circuits)
(Bus protocols: RS232, USB, I2C, SPI, …))

## Slide 10: Electronics: Digital Inputs
Digital input:
0 Volt: Low
5 Volt: High
2.5 Volt or floating?:
  Undefined !!

## Slide 11
Electronics : Digital sensors
Notes: Button, Tilt switch, rotation sensor, IR photo gate , Optocoupler

## Slide 12: Electronics: Digital Inputs
External pull up Internal pull up Internal pull up (new)
pinMode(12, INPUT); pinMode(12, INPUT); pinMode(12,INPUT_PULLUP);
digitalWrite(12, LOW); digitalWrite(12, HIGH); int a = digitalRead(12);
int a = digitalRead(12); int a = digitalRead(12);
5V
Arduino
GND
100K
switch
Arduino
GND
20K
switch
5V

## Slide 13: Electronics: Analog Inputs
Analog input:
Default:
  0..5 Volt to 0..1023
  0 => 0
  2,5 => 512
  5 => 1023

## Slide 14
Electronics : Analog sensors
Notes: Accelerometer, microphone, LDR, Flex sensor, Photodiode, FSR, NTC

## Slide 15: Electronics: Analog Inputs
pinMode(A0, INPUT);
Int a = analogRead(A0);
5V
Arduino
GND
10K
A0

## Slide 16: Electronics: Digital Outputs
Digital output:
0 Volt: Low
5 Volt: High
2.5 Volt? NO
PWM and average voltage for a number of duty cycles
(“PWM” : ~ pins)

## Slide 17
Electronics : Actuators

## Slide 18: Electronics: Digital Outputs
pinMode(13, OUTPUT); pinMode(11, OUTPUT);
digitalWrite(13, LOW); analogWrite(11, 186);
digitalWrite(13, HIGH);
Arduino
GND
330Ω
LED

## Slide 19: Electronics: Digital Outputs
Bang
Digital output:
0 Volt: Low
5 Volt: High

## Slide 20: Electronics: Digital Outputs
Digital output:
0 Volt: Low
5 Volt: High
External Power
< 20mA
Amp

## Slide 21: Some Hardware Limitations (Arduino Uno)
The Uno can be powered via USB or external power supply; power source is selected automatically. Usually a PC USB port is power limited to 100 mA max.
External (non-USB) power can come from an AC-to-DC adapter or battery. The adapter can be connected into the board's power jack. Leads from a battery can be inserted in the Gnd and Vin pin headers of the POWER connector.
Operating Voltage 5 V
Input Voltage (recommended) 7-12 V, (limits) 6-20 V. If the Uno is supplied with less than 7 V, the 5 V pin may supply less than five volts and the board may be unstable. If using more than 12 V, the voltage regulator may overheat and damage the board
DC Current per I/O pin max. 40 mA
DC Current for 3.3 V pin max. 50 mA
Depending on supply voltage and current usage (including the current for the processor) the voltage regulator may overheat and stop working until it has cooled down. Generally driving one servo or a few normal LEDs is the maximum.

## Slide 22: The IDE program
Arduino board
USB port
A compiled “hex”-file is
sent to the program
memory of the Arduino board
Acts as serial

## Slide 23: The program
First, tell Arduino what it is:
Declare pins as input or output
Set global variables
This is done only once
immediately after reset
Then tell it what to do:
Read inputs
Do calculations
Set outputs
This is done continuously,
in a loop after setup is finished

## Slide 24: The program
/* Configuration:
First, tell Arduino what it is */
void setup() {
// initialize the digital pin as an output.
// Pin 13 has a LED connected on most Arduino boards: pinMode(13, OUTPUT);
}
/* Then loop:
Tell Arduino what to do */
void loop() {
digitalWrite(13, HIGH); // switch LED on
delay(1000); // wait for a second
digitalWrite(13, LOW); // switch LED off
delay(1000); // wait for a second
}

## Slide 25: Compiling and uploading code
Type code in text window
Push ‘upload’ button
Check if TX and RX Leds are blinking rapidly
If the ‘Done uploading’ message displays, the Arduino is ready.
1
2
3
4

## Slide 26: www.arduino.cc
Everything you need is www.arduino.cc
Getting started
Reference
Tutorials
Hardware examples
Software examples

## Slide 27: The Arduino Programming Environment
Compile and Upload
Verify (Compile)
Open Sketch (old: *.pde, new: *.ino)
Save Sketch
New Sketch

## Slide 28: Settings
Let the Arduino programming environment know which board you have
  “Tools” menu  “Board”
Let the Arduino programming environment know to which port the board is connected
  “Tools” menu  “Serial port”

## Slide 29: Blink
/* comment */
void setup() {
// initialize the digital pin as an output.
// Pin 13 has a LED connected on most Arduino boards: pinMode(13, OUTPUT);
}
void loop() {
digitalWrite(13, HIGH); // switch LED on
delay(1000); // wait 1000 ms
digitalWrite(13, LOW); // switch LED off
delay(1000); // wait 1000 ms
}

## Slide 30: Blink with button
The period of “Blink” is 2 x 1000 ms = 2 s
Now we want: if we push a button, the period should become 0.5 s
To do:
  Connect a button
  Read a button
  Change the “1000” in “delay” depending on the button state

## Slide 31: Blink and read button
/* comment */
void setup() {
// initialize digital pin 13 as an output.
// Pin 13 has a LED connected on most Arduino boards: pinMode(13, OUTPUT);
pinMode(12, INPUT); // initialize digital pin 12 as input.
digitalWrite(12, HIGH); // activate pull-up resistor
}
void loop() {
digitalWrite(13, HIGH); // switch LED on
delay(1000); // wait one second
digitalWrite(13, LOW); // switch LED off
delay(1000); // wait one second
}

## Slide 32: Possible hardware for Blink with button
Switch
LED

## Slide 33
void setup() {
// initialize the digital pin 13 as an output.
// Pin 13 has a LED connected on most Arduino boards: pinMode(13, OUTPUT);
pinMode(12, INPUT); // initialize digital pin 12 as input.
digitalWrite(12, HIGH); // activate pull-up resistor
}
void loop() {
if (digitalRead(12) == HIGH) {
// Do something
}
else {
// Do something else
}
digitalWrite(13, HIGH); // switch LED on
delay(1000); // wait one second
digitalWrite(13, LOW); // switch LED off
delay(1000); // wait one second
}

## Slide 34
int wait = 1000;
void setup() {
…
}
void loop() {
if (digitalRead(12) == HIGH) {
// Do something
}
else {
// Do something else
}
digitalWrite(13, HIGH); // switch LED on
delay(wait); // wait for wait msec
digitalWrite(13, LOW); // switch LED off
delay(wait); // wait for wait msec
}

## Slide 35
int wait = 1000;
void setup() {
…
}
void loop() {
if (digitalRead(12) == HIGH) {
wait = 1000; // Wait 1 sec
}
else {
wait = 250; // Wait 0.25 sec
}
digitalWrite(13, HIGH); // switch LED on
delay(wait); // wait for wait msec
digitalWrite(13, LOW); // switch LED off
delay(wait); // wait for wait msec
}

## Slide 36: Create some interaction: The “Physical Pixel” example
const int ledPin = 13; // the pin that the LED is attached to
int incomingByte; // a variable to read incoming serial data into
void setup() {
Serial.begin(9600); // initialize serial communication
Serial.println(”Good morning”); // Send text to computer
pinMode(ledPin, OUTPUT); // initialize LED pin as output
}
void loop() {
if (Serial.available() > 0) {
incomingByte = Serial.read();
if (incomingByte == 'H') digitalWrite(ledPin, HIGH);
if (incomingByte == 'L') digitalWrite(ledPin, LOW);
}
}

## Slide 37: How to proceed?
Find new functions in the reference (http://arduino.cc/en/Reference/HomePage)
Arduino playground Manuals and Curriculum (also downloads) (http://playground.arduino.cc/Main/ManualsAndCurriculum)
Don’t be scared by “Making things talk”: the book is about connecting to the internet and less to interfacing with electronics

## Slide 38: Available examples
For descriptions see http://arduino.cc/en/Tutorial/HomePage

## Slide 39: The mini project
Session Dec 8 team presents mini project proposal (HG 4.24 Group1 / HG 4.57 Group2)
Session Dec 11 and Dec 15 no lecture, but support in and around e-Atelier/ID-Café for mini project development
Session Dec 18 (HG 4.57) team presents mini project result (demo + mini poster) to assignor

## Slide 40: The mini project
You are free to choose your project, but:
  Use Arduino if possible
  Use at least one sensor and one actuator
  Report on design choices (transistor, configuration, etc.)
  Draw schematics
  Present it as a prototype (user experience, packaging) !

## Slide 42: Suggestions
Make the central heating system with Arduino
μC
Temp.
Set
Heater

## Slide 43: Suggestions
Dim a LED
Make application / context
μC
Set

## Slide 44: Suggestions
Egg timer
μC
Soft
Middle
Hard

## Slide 45: Spaghetti in code, schematics and circuits
Code:
Use comments /* like this */ or // this
Use functional variable names
Use functions
Schematics:
Draw the complete circuit (correctly!!)
(component names, values)
Circuit (soldered or breadboard)
Should be structured
Use color coding in wires
Think about component placement
Otherwise:
Debugging becomes difficult
You lack evidence in your report

## Slide 46: Code
Code:
Clear variable names
Proper use of local and global variables
Functions setup() and loop() are self-explaining
Proper function names
Comments (Header)
Examples
  Bad example
  Good example

## Slide 47: Schematics

## Slide 48: Circuits

## Slide 49
Poster
Explanation
Schematic
Code
Pictures

## Slide 50
Resources
Look at wiki page:
  http://wiki.id.tue.nl/ce/AssignmentDescription
  (and checkout the “Resources” section)
Installation
  http://arduino.cc/en/Guide/Windows
  http://arduino.cc/en/Guide/MacOSX