## Slide 1: Arduino

## Slide 2
Arduino Hardware
Blink an LED
Digital Input
Analog Input
Analog Output
Serial Communication
  Using Serial Libraries
  Using Firmata

## Slide 3: Why Arduino?
Physical Computing
  uses electronics
  to prototype new materials
  for designers and artists.
Tinkering
Patching
Community
  Blog, Forum, Playground (wiki)

## Slide 4: Hardware

## Slide 5: UNO

## Slide 6: UNO
Microcontroller | ATmega328
Operating Voltage | 5V
Input Voltage (VIN) (recommended) | 7-12V
Input Voltage (limits) | 6-20V
Digital I/O Pins | 14 (of which 6 provide PWM output)
Analog Input Pins | 6
DC Current per I/O Pin | 40 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 32 KB (ATmega328) of which 0.5 KB used by bootloader
SRAM (Static RAM) | 2 KB (ATmega328)
EEPROM (Electrically erasable programmable ROM) | 1 KB (ATmega328)
Clock Speed | 16 MHz

## Slide 7: UNO
Power: USB Power supply (5V)
VIN

## Slide 8: UNO
Power: external power supply (7V-12V)
VIN

## Slide 9: UNO
Power: VIN, input or supply, depending on external power source. (7-12V)
VIN

## Slide 10: UNO
Power: 5V supply
VIN

## Slide 11: UNO
Power: 3.3V supply
VIN

## Slide 12: UNO
Power: GND pins
VIN

## Slide 13: UNO
Digital I/O Pins 14 (of which 6 provide PWM output)

## Slide 14: UNO
Digital I/O Pins 14 (of which 6 provide PWM output)
  PWM (Pulse-width modulation)

## Slide 15: UNO
Serial: 0 (RX) and 1 (TX)

## Slide 16: UNO
LED: 13

## Slide 17: UNO
6 analog inputs, 10 bits of resolution (i.e. 1024 different values)

## Slide 18: UNO
AREF: Reference voltage for the analog inputs

## Slide 19: UNO
Reset. LOW to reset the microcontroller

## Slide 20: Software: IDE
http://arduino.cc/en/Main/Software

## Slide 21: Driver Installation and Port Identification
Refer to the instructions in
  “Getting Started with Arduino”, page 23-26

## Slide 22: Breadboard

## Slide 23: Color coding of the resistors

## Slide 24: Really getting started

## Slide 25: Blinking an LED
File>Examples>Basics>Blink
  LED: light-emitting diode

## Slide 26: Blinking an LED

## Slide 27: Blink an LED
#define LED 13

## Slide 28: Button to control the LED
File>Examples>Digital>Button

## Slide 29: Button to control the LED

## Slide 30: Button to control the LED

## Slide 31: Button to control the LED

## Slide 32: Analog I/O
File>Examples>Analog>AnalogInput
  Instead of a potentiometer, we use a light sensor

## Slide 33: Analog I/O

## Slide 34: Analog I/O

## Slide 35: Analog I/O

## Slide 36: Serial Communication
We are going to use the Serial library from Processing to talk to Arduino
  http://processing.org/reference/libraries/serial/index.html
In Processing
  File>Examples>Books>Getting Started>Ex_11_06
  You can not run this program in Processing
  Copy the code to Arduino software, upload to Arduino.

## Slide 37: Serial Communication

## Slide 38: Serial Communication

## Slide 39: Serial Communication

## Slide 40: Serial Communication
In Processing
  File>Examples>Books>Chapter 11>Ex_11_07

## Slide 41: Serial Communication

## Slide 42: Serial Communication

## Slide 43: Serial Communication

## Slide 44: Serial Communication

## Slide 45: Serial Communication
Introducing Firmata
  http://playground.arduino.cc/Interfacing/processing

## Slide 46: Serial Communication
Introducing Firmata
  http://playground.arduino.cc/Interfacing/processing

## Slide 47: Serial Communication
Introducing Firmata
  http://playground.arduino.cc/Interfacing/processing

## Slide 48: Serial Communication
Introducing Firmata
  http://playground.arduino.cc/Interfacing/processing

## Slide 49: That was Arduino.